## Slide 1: Irobot ii
Creating garden monitoring device
Prepared by: engr. Ronchester sigfrid mendoza

## Slide 2: Components
POWER SUPPLY
LCD SCREEN
SENSORS
PROCESSOR

## Slide 3
POWER SUPPLY
A power supply is an electrical device that supplies electric power to an electrical load
The primary function of a power supply is to convert electric current from a source to the correct voltage, current, and frequency to power the load
Typical 5V power supply

## Slide 4: War of the Currents
Both AC and DC describe types of current flow in a circuit.
In direct current (DC), the electric charge (current) only flows in one direction.
Electric charge in alternating current (AC), on the other hand, changes direction periodically.
Notes: History
Tesla is a former employee of DC creator, Thomas Edison in 1890
Tesla patented AC as new form of current
Edisons company was threathened when Tesla solds his patents to Westinghouse, a business investor, in order to create a Americas new grid
As attempt to overthrew the AC idea to the public, Edison produces stunts such as using AC to electrocute stray dogs, an Elephant, and produce the 1st victim of Electric Chair
But this didn’t stop the 2 partners. They won a bid to produce a large scale power grid. A literal waterfall landslide loss to Edison. Westinghouse build the power grid generator in Niagra Falls
which provides almost 50% of America

## Slide 5: USE OF DC AND AC
Most of the digital electronics that you use will use DC.
AC also has some useful properties, such as being able to convert voltage levels with a single component (a transformer), which is why AC was chosen as the primary means to transmit electricity over long distances.

## Slide 6: Converting AC to DC
Transformers steps down the voltage input based on turns ratio of primary and secondary
Rectifiers converts AC input voltage to pulsating DC voltage
Filters eliminates fluctuations and tries to produce a smooth DC voltage
Regulator maintains a constant DC voltage for the load
Basic block diagram of complete power supply []

## Slide 7: Choosing your power supply
Determine how much wattage you need

## Slide 8
LCD SCREEN
A liquid-crystal display (LCD) is a flat-panel display to produce a visible image.
LCD are super-thin technology display screen that are generally used in laptop computer screen, TVs, cell phones and portable video games
16×2 LCD Display

## Slide 9: Liquid crystal display
Visual display used in electronic devices
Displays Alphanumeric Symbols
Low Power Display
Pinout of LCD Screen
Operating Voltage: 5 VDC
DISPLAY: 16x2 Characters

## Slide 10: Test code
LCD Screen connection to Arduino Uno
*LiquidCrystal.h Library used is the standard library in Arduino IDE

## Slide 11
SENSORS
DHT22 Digital Sensor & Soil Moisture Sensor
Sensors are sophisticated devices that are frequently used to detect and respond to electrical or optical signals.
A Sensor converts the physical parameter (for example: temperature, blood pressure, humidity, speed, etc.) into a signal which can be measured electrically.
Electrical signals can be interpreted by processors for humans to read

## Slide 12: Dht22 Digital temperature and humidity sensor
Includes a capacitive sensor wet components and a high-precision temperature measurement devices
Standard single-bus interface, system integration quick and easy
signal transmission distance up to 20 meters, making it the best choice of all kinds of applications and even the most demanding applications
Pinout of DHT22
Supply voltage: 5V
Output voltage: 0-3.3V
Temperature range:-40-80℃ resolution0.1℃ error <±0.5℃
Humidity range:0-100%RH resolution0.1%RH error±2%RH

## Slide 13: Test Code
DHT22 connection to Arduino Uno
*DHT.h Library used is from Seed Studio Grove Temperature And Humidity Sensor

## Slide 14: Soil Moisture sensor
Pinout of Capacitive Soil Sensor
SIG
VCC
GND
Our soil moisture sensor measures soil moisture levels by capacitive sensing
Made of corrosion resistant material which gives it an excellent service life
Operating Voltage: 3.3 ~ 5.5 VDC
Output Voltage: 0 ~ 3.0VDC
Operating Current: 5mA

## Slide 15: Calibration Test Code
Soil Moisture Sensor connection to Arduino Uno

## Slide 16: Test Code 2
Soil Moisture Sensor connection to Arduino Uno

## Slide 17: System integration

## Slide 18: Sources
[1] Arduino LCD Tutorial https://howtomechatronics.com/tutorials/arduino/lcd-tutorial/
[2] Basic DC Power Supply Circuit https://engineeringtutorial.com/basic-dc-power-supply-circuit/
[3] Sensors: Different Types of Sensors https://www.engineersgarage.com/articles/sensors
[4] DFRobot Soil Moisture Sensor https://wiki.dfrobot.com/Capacitive_Soil_Moisture_Sensor_SKU_SEN0193

## Slide 19: Contact details
someone@example.com